## Slide 1: What is Exchange Hybrid?

## Slide 2
Thomas Stensitzki
Enterprise Consultant | Owner Granikos GmbH & Co. KG
MVP | Office Apps & Services MCT Regional Lead Email thomas.stensitzki@granikos.eu Twitter @Stensitzki LinkedIn https://linkedin.com/in/thomasstensitzki
Blog http://JustCantGetEnough.Granikos.eu Web https://www.stensitzki.de

## Slide 3: What is Exchange Hybrid?
"Dieses Foto" von Unbekannter Autor ist lizenziert gemäß CC BY

## Slide 4: What is Exchange Hybrid?
On-Premises Exchange Organization
Microsoft 365
Exchange Online
Hybrid Configuration
Trusted relationship between an on-premises Exchange Organization and Exchange Online
Hybrid connections for mail flow (SMTP), and service access (HTTPS) for Exchange hybrid functionality
Hybrid Configuration Wizard (HCW) activates and configures the hybrid mode of operation

## Slide 5: Exchange Hybrid
Hybrid Mode
Classic
Express
Minimal
Modern
Minimal
Full
Full
Two Modes – Three Variants

## Slide 6: Classic Full Hybrid
On-Premises Exchange Organization
Hybrid Configuration
Perimeter Network
Microsoft 365
Exchange Online
Azure AD
Company Network
SMTP
HTTPS
Active Directory Hybrid with Azure AD Connect
  Exchange Hybrid option enabled
SMTP Connection between On-Premises and Exchange Online
  Separate hostname (e.g., smtp365.company.com)
  Additional public IP address
  TLS certificate for hostname
  Edge Transport Role in perimeter network (1)
  Alternatively, direct inbound connection (2)
Inbound HTTPS connection to Client Access Service
  Internal Exchange Servers published by a Reverse Proxy
  Requires additional public IP address
Outbound HTTPS connections to Exchange Online
  Exchange Server communication to Exchange Online

## Slide 7: Modern Full Hybrid
Active Directory Hybrid with Azure AD Connect
  Exchange Hybrid option enabled
SMTP Connection between On-Premises and Exchange Online
  Separate hostname (e.g., smtp365.company.com)
  Additional public IP address
  TLS certificate for hostname
  Edge Transport Role in perimeter network (1)
  Alternatively, direct inbound connection (2)
Outbound HTTPS connections to Exchange Online
  Exchange Hybrid-Agent Exchange Online to Exchange on-premises communication
  Exchange Server communication to Exchange Online
Install additional Hybrid-Agents for redundancy
Hybrid Configuration
Perimeter Network
Microsoft 365
Exchange Online
Azure AD
Company Network
On-Premises Exchange Organization
HTTPS
SMTP

## Slide 8: Exchange Hybrid
Full
Full classic hybrid configuration, Exchange server published to the internet (SMTP/HTTPS)  permanent hybrid operation and Teams access to on-premises
Minimal
Hybrid configuration, without rich coexistence to migrate all on-premises mailboxes to Exchange Online  temporary hybrid operation for a few weeks / months
Express
Hybrid configuration, with Azure AD Connect Express settings, to migrate all on-premises mailboxes to Exchange Online  temporary hybrid operation for a few days / weeks
Full
Full Modern Hybrid configuration, for new hybrid setups based on Hybrid Agent deployment, with reduced hybrid functionality  permanent hybrid operation
Minimal
Modern Hybrid configuration, to migrate all on-premises mailboxes to Exchange Online  temporary hybrid operation for a few weeks / months
The Differences

## Slide 9: Why do you need Exchange Hybrid?

## Slide 10: Why do you need Exchange Hybrid?
Coexistence between your on-premises Exchange Organization and Exchange Online
Mailbox migration to and from Exchange Online
Seamless public folder migration to Exchange Online
Microsoft Teams with on-premises mailboxes (calendar access)
Transition from an on-premises Exchange Organization to Exchange Online
Optimal migration experience for end users
Centralized mail flow for use of on-premises email solutions with user mailboxes in Exchange Online
  Gateway-based S/MIME decryption/encryption, email disclaimer, archiving, journaling, …
Hybrid mail flow providing email relay functionality for on-premises legacy applications and devices with
  No access to the internet
  No support for TLS protocols 1.0 or 1.1
  No support for SMTPAUTH user authentication
  No support for SMTP modern authentication

## Slide 11: Exchange Hybrid Recommendations
On-Premises Exchange Server 2019 hybrid endpoint
  Microsoft Teams backend services use AutoDiscover v2 to discover on-premises EWS and REST endpoints
  Client Access Endpoint accessible for Microsoft Teams backend services
  Always use latest Exchange Server cumulative update
  In-Place upgrade capability for Exchange Server vNEXT (H2 2021)
Use Third-Party TLS-certificate with all required subject alternate names (SAN) for incoming HTTPS connections
  AutoDiscover
  Exchange namespace  Exchange Virtual Directory’s external URL-Settings
Use a dedicated Third-Party TLS-certificate for SMTP when using centralized mail flow
Enable and configure OAUTH authentication using Hybrid Configuration Wizard
  Exchange team provides detailed information on how to configure OAUTH manually
AutoDiscover DNS resource records for SMTP domains used for primary email addresses
Use Exchange Server 2016 if you need a coexistence server only

## Slide 12: How to implement Exchange Hybrid?

## Slide 13: Exchange Hybrid Requirtements
Know the differences of the Exchange hybrid variants and modes of operation available
Know the mode of operation for your Exchange Organization and hybrid requirements
Have your on-premises Exchange organization ready for hybrid configuration
Install latest Exchange Server Cumulative Updates on all Exchange Servers, including Edge Transport
Have required IP addresses & DNS hostnames for the Exchange namespace set up
Verify inbound connectivity to your Exchange organization using Remote Connectivity Analyzer (RCA)
  When your firewall policy is restricted for inbound traffic, add the RCA IP addresses to that policy  RCA release notes
Have Edge Transport TLS certificates installed on internal an Exchange Server for selection by HCW, when using Edge
  Do NOT enable this certificate for any Exchange service
Enable Exchange Hybrid option in Azure AD Connect first

## Slide 14: Hybrid Configuration Wizard
Click-2-Run Setup
  https://aka.ms/HybridWizard
  .application file type requires mapping to Internet Explorer
Note the HCW version information
  Current: v17
  Uninstall v16 first
HCW is updated regularly
  HCW downloads a newer version automatically when started
HCW configuration steps vary depending on your Exchange Organization configuration

## Slide 15: Hybrid Configuration Wizard
HCW detects the optimal Exchange Server for configuration automatically
Specify a CAS server manually, if needed
Select the appropriate Office 365 target infrastructure
  Office 365 Worldwide is the default for commercial customers
On-Premises Organization

## Slide 16: Hybrid Configuration Wizard
HCW connects to on-premises Exchange and Exchange Online to gather the current organizational configuration
  Adjust credentials as needed
 Check, if WinRM allows Basic Authentication
Gathering Organization Configuration

## Slide 17: Hybrid Configuration Wizard
Select hybrid features to configure
  Minimal Hybrid
  Full Hybrid
Enable Organization Configuration Transfer
  One-time transfer of selected configuration objects
  Available objects depend on the on-premises Exchange Server version
Hybrid Organization Configuration Transfer Documentation
Hybrid Features

## Slide 18: Hybrid Configuration Wizard
Select Hybrid Topology
  Exchange Classic Hybrid
  Exchange Modern Hybrid
Modern Hybrid uses the Modern Hybrid Agent
  Azure Application Proxy-style component using HTTPS outbound connectivity only
Automatic download and installation of
  Hybrid Updater
  Hybrid Agent
HCW uninstalls and unregisters the Modern Hybrid Agent when switching from Modern Hybrid
Hybrid Topology

## Slide 19: Hybrid Configuration Wizard
Configure hybrid mail flow
  Direct to/from internal Exchange Servers
  Via Edge Transport Servers in perimeter network, already subscribed to Active Directory site
Centralized mail flow
  Route all mail flow to/from Exchange Online mailboxes via on-premises Exchange Organization
Hybrid Mail Flow

## Slide 20: Hybrid Configuration Wizard
Select the Exchange server used for receiving email messages from Exchange Online
  Select the Exchange Server published to the Internet
  HCW configures the default frontend receive connector
HCW might select the wrong receive connector
  You use additional receive connectors with a remote IP address range 0.0.0.0 – 255.255.255.255
  The default frontend connector uses individual remote IP address ranges configuration
  Compare TlsCertificateName and TlsDomainCapabilities connector properties afterwards
Receive Connector

## Slide 21: Hybrid Configuration Wizard
Select Exchange server for sending email messages from the on-premises Exchange Organization to Exchange Online
  HCW configures Send Connector
  Exchange Server needs outbound connectivity to Exchange Online
  EdgeSync transfers the Edge Servers’ Send Connector configuration (when using Edge Transport)
Send Connector

## Slide 22: Hybrid Configuration Wizard
Select TLS certificate to secure the trusted mail flow between on-premises Exchange and Exchange Online
With Edge Transport
  Ensure that the dedicated TLS certificate is installed in the certificate store of one of the internal Exchange servers
  Import the TLS certificate prior to executing HCW into the local Exchange Server certificate store
  Do NOT enable the TLS certificate for any Exchange service
  Avoid using NAT between Edge Transport Servers and internal Exchange servers
  Do NOT use TLS intercepting SMTP proxy servers
Transport Certificate

## Slide 23: Hybrid Configuration Wizard
Enter the external FQDN of the Exchange Organization for inbound SMTP
  Hostname should match TLS certificate
Hybrid mail flow requires Exchange to Exchange communication
Recommendation for centralized mail flow
  Use a dedicated host name, IP address, and TLS certificate
  Use Edge Transport Server(s)
Organization FQDN

## Slide 24: Hybrid Configuration Wizard
Update and wait
If updating fails
  HCW provides full log files  %appdata%\Roaming\Microsoft\Exchange Hybrid Configuration
  Log file contains all PowerShell configuration steps
  Use Remote Connectivity Analyzer to check inbound connectivity
Issues
  Remote connectivity  Firewall policies, proxy servers, DNS
  WinRM Windows service configuration issues

## Slide 25: Microsoft Teams and Exchange Server

## Slide 26: Microsoft Teams and Exchange Server
Microsoft Teams Client communicates with Teams Middle-Tier, not with Exchange directly
Microsoft Teams Middle-Tier contacts Exchange Online first
  If user mailbox is not in Exchange Online, the Teams Backend receives an HTTP 302 Redirect to On-Premises
  On-premises endpoint is always discovered using AutoDiscover v2
Exchange Redirect requires AAD Connect synchronization with Exchange Hybrid option enabled
Authentication requires OAuth between Exchange Server and Exchange Online / Azure AD
  Use Hybrid Configuration Wizard to configure OAuth (preferred)
Microsoft Teams Backend requires communication with AutoDiscover, EWS, and REST endpoints

## Slide 27: Microsoft Teams and Exchange Server
When using many different SMTP domain names, you need a dedicated AutoDiscover v2 endpoint for each domain
  Microsoft Teams backend services do not handle an on-premises HTTP 302 redirect correctly
  Publish an AutoDiscover endpoint for each SMTP domain
  Use an edge router if you cannot add all domains to a single SAN certificate, e.g., Traeffic
Check Microsoft Teams Coexistence mode with Skype for Business Online
  Only Island, Teams Only, or Skype for Business with Teams Collaboration and Meeting support the calendar tab
Verify that the calendar tab is enabled in Teams App Policy
Ensure that Exchange Hybrid is enabled in Azure AD Connect

## Slide 28
Thomas Stensitzki
Enterprise Consultant | Owner Granikos GmbH & Co. KG
MVP | Office Apps & Services Email thomas.stensitzki@granikos.eu Twitter @Stensitzki LinkedIn https://linkedin.com/in/thomasstensitzki
Blog http://JustCantGetEnough.Granikos.eu Web https://www.stensitzki.de

## Slide 29: Ressources
Exchange Server Hybrid Deployments
Hybrid Deployment Prerequisites
Hybrid Configuration Wizard FAQs
Configuring Teams calendar access for Exchange on-premises mailboxes
Configure OAuth authentication between Exchange and Exchange Online organizations
Demystifying and troubleshooting hybrid mail flow: when is a message internal?
Remote Connectivity Analyzer
How Exchange and Microsoft Teams interact
Traeffic Edge Router