## Slide 1: Exchange User Group Berlin {Online Edition}
25. Mai 2020

## Slide 2: Exchange Server Hybrid
Was ist das? Warum brauche ich das? Wie geht das?

## Slide 3
Thomas Stensitzki
Enterprise Consultant Granikos GmbH & Co. KG MVP | MCT Regional Lead | MCSM @stensitzki thomas.stensitzki@granikos.eu

## Slide 4: What is Exchange Hybrid?
Trusted relationship between an on-premises Exchange Organization and Exchange Online
Hybrid connections for mail flow (SMTP), and client access (HTTPS) for hybrid functionality
Hybrid Configuration Wizard (HCW) activates and configures the hybrid mode of operation
On-Premises Exchange Organization
Microsoft 365
Exchange Online
Hybrid Configuration

## Slide 5: Exchange Hybrid Benefits
Free Busy lookups
No recreating of Outlook Profiles
Mailbox migrations without user interruption
Seamlessly connect to on-premises & Exchange Online
One Global Address List
Secure Mail Flow between on-premises & Exchange Online
Hybrid Modern Authentication
Cloud based archiving
And much more…

## Slide 6: Exchange Hybrid | Two Variants – Three Modes
Hybrid Configuration
Classic
Express
Minimal
Modern
Minimal
Full
Full

## Slide 7: Classic Full Hybrid
Active Directory Hybrid with Azure AD Connect
  Exchange Hybrid enabled
SMTP Connection between On-Premises and Exchange Online
  Separate hostname (e.g., smtp365.company.de)
  Additional public IP address
  TLS certificate for hostname
  Edge Transport Role in perimeter network (A)
  Alternatively, direct inbound connection (B)
Inbound HTTPS connection to Client Access Service
  Published by Reverse Proxy
  Additional public IP address
Outbound HTTPS connections to Exchange Online
  Exchange Server
On-Premises Exchange Organization
Hybrid Configuration
Perimeter Network
Microsoft 365
Exchange Online
Azure AD
Company LAN
SMTP
HTTPS
A
B

## Slide 8: Modern Full Hybrid
Active Directory Hybrid with Azure AD Connect
  Exchange Hybrid enabled
SMTP Connection between On-Premises and Exchange Online
  Separate hostname (e.g., smtp365.company.de)
  Additional public IP address
  TLS certificate for hostname
  Edge Transport Role in perimeter network (A)
  Alternatively, direct inbound connection (B)
Outbound HTTPS connections to Exchange Online
  Exchange Hybrid-Agent (Exchange Online to Exchange on-premises communication)
  Exchange Server
Hybrid Configuration
Perimeter Network
Microsoft 365
Exchange Online
Azure AD
Company LAN
On-Premises Exchange Organization
HTTPS
SMTP
A
B

## Slide 9: Exchange Hybrid – The Differences
Full
Full classic hybrid configuration, Exchange server published to the internet (SMTP/HTTPS)  permanent hybrid operation
Minimal
Hybrid configuration, without rich coexistence to migrate all on-premises mailboxes to Exchange Online  temporary hybrid operation for a few weeks / months
Express
Hybrid configuration, with Azure AD Connect Express settings, to migrate all on-premises mailboxes to Exchange Online  temporary hybrid operation for a few days / weeks
Full
Full Modern Hybrid configuration, for new hybrid setups based on Hybrid Agent deployment, with reduced hybrid functionality  permanent hybrid operation
Minimal
Modern Hybrid configuration, to migrate all on-premises mailboxes to Exchange Online  temporary hybrid operation for a few weeks / months

## Slide 10: Exchange Server Hybrid
Was ist das? Warum brauche ich das? Wie geht das?

## Slide 11: Why do you need Exchange Hybrid?
Coexistence between on-premises Exchange Organization & Exchange Online
Mailbox migration to/from Exchange Online
Microsoft Teams with on-premises mailboxes
Transition from on-premises Exchange to Exchange Online
Optimal migration experience for end users
Centralized mail flow for use of on-premises mail solutions and cloud-hosted mailboxes
  Gateway-based S/MIME de-/encryption, disclaimer, archiving, journaling, …
Hybrid mail flow providing Exchange relay functionality for on-premises legacy applications and devices
  No access to the internet
  No support for TLS connection encryption
  No support for user authentication

## Slide 12: Exchange Hybrid and Microsoft Teams
On-Premises Exchange Server 2016 / 2019 hybrid endpoint
  Microsoft Teams backend uses AutoDiscover v2
  Client Access Endpoint for Microsoft Teams backend services
  Always run latest Exchange Server cumulative update
Use Third-Party TLS-certificate
Enable Hybrid Modern Authentication
AutoDiscover public DNS resource records for SMTP domains

## Slide 13: Exchange Server Hybrid
Was ist das? Warum brauche ich das? Wie geht das?

## Slide 14: Exchange Hybrid Requirements
Know the different hybrid variants and modes
Know your target operation mode for Exchange hybrid
Have your on-premises Exchange organization in good shape
  Latest cumulative updates installed
Verify inbound connectivity to your Exchange organization using Remote Connectivity Analyzer
Have required IP addresses & DNS host names set up
Edge Transport Server is subscribed to the Active Directory Site
Have Edge TLS certificates installed on internal Exchange Servers for selection by HCW
  Not enabled for any Exchange service

## Slide 15: Hybrid Configuration Wizard
Exchange Server Requirements
  Exchange 2010 SP3 + latest Update Rollup
  Exchange 2013 CU1 or later
  Exchange 2016 and Exchange 2019
   Supported modern Exchange Server setup requires latest CU (or N-1)
Click-2-Run Setup
  https://aka.ms/HybridWizard
  Ensure that .application file extension is mapped to Internet Explorer
Current Version 17.x
  Uninstall HCW 16.x first
Verify that WinRM service is running and not controlled by GPO

## Slide 16: Hybrid Configuration Wizard
Note the HCW version information
HCW is updated regularly

## Slide 17: Hybrid Configuration Wizard
Optimal Exchange Server detected by HCW
Specify a CAS server manually, if needed
Select Office 365 target infrastructure
On-Premises Exchange Server Organization

## Slide 18: Hybrid Configuration Wizard
Connect to on-premises Exchange and Exchange Online
  Adjust credentials as needed
Check, if WinRM allows Basic Authentication
Administrative Exchange Accounts

## Slide 19: Hybrid Configuration Wizard
Select hybrid features
  Minimal Hybrid
  Full Hybrid
Enable Organization Configuration Transfer
  One-time transfer of selected configuration objects
Hybrid Features

## Slide 20: Hybrid Configuration Wizard
Select Hybrid Topology
  Classic Hybrid
  Modern Hybrid
Hybrid Topology

## Slide 21: Hybrid Configuration Wizard
Configure credentials for on-premises Exchange Web Service Endpoint
  Used for mailbox migrations
Migration Account

## Slide 22: Hybrid Configuration Wizard
Hybrid Agent Setup starts automatically
  Download and install of Hybrid Updater
  Download and install of Hybrid Agent
Hybrid Agent Setup

## Slide 23: Hybrid Configuration Wizard
Configure hybrid mail flow
  Direct to/from internal Exchange Servers
  Edge Transport Servers in perimeter network
Centralized mail flow
  Route all mail flow to/from Exchange Online via on-premises Exchange Organization
Hybrid Mail Flow

## Slide 24: Hybrid Configuration Wizard
Select Exchange server used for receiving email messages from Exchange Online
  Select the Exchange Server published to the Internet
  HCW configures the receive connector
Receive Connectors

## Slide 25: Hybrid Configuration Wizard
Select Exchange server for sending email messages from the on-premises Exchange Organization to Exchange Online
  HCW configures Send Connectors
  Server needs outbound connectivity to Exchange Online
Send Connectors

## Slide 26: Hybrid Configuration Wizard
Select TLS certificate to secure the trusted mail flow between on-premises Exchange and Exchange Online
With Edge Transport
  Ensure that the dedicated TLS certificate is installed in the certificate store of one of the internal Exchange servers
  Do NOT enable the TLS certificate for any Exchange service
Transport Certificate

## Slide 27: Hybrid Configuration Wizard
Enter the external FQDN of the Exchange Organization
  Hostname should match TLS certificate
Inbound SMTP Host Name

## Slide 28: Hybrid Configuration Wizard
Update and wait
If it fails
  HCW provides access to full log files
  All configuration steps documented
  Remote Connectivity Analyzer to check inbound connectivity
Issues
  Remote connectivity
   Firewall, Proxy, DNS
  WinRM Windows service configuration issues
Ready for Update

## Slide 29: Q & A
Supportende
13. Oktober 2020

## Slide 30: Ressourcen
Exchange Server Hybrid Deployments
Hybrid Deployment Prerequisites
Hybrid Configuration Wizard FAQs
How to configure Exchange Server on-premises to use Hybrid Modern Authentication
How Exchange and Microsoft Teams interact
Configure OAuth authentication between Exchange and Exchange Online organizations
Remote Connectivity Analyzer